## Slide 1: Smart Agriculture
LIU CHANG

## Slide 2: Introduction

## Slide 3: System Architecture
A network with two type of Protocols:
MQTT
  Humidity Sensors
  Temperature Sensors
CoAP
  Sprinklers Actuators
A Java Collector that:
Receives data from sensors
Executes control logic
Writes to a MySQL database
Exposes a CLI
A Web interface Using Grafana

## Slide 4: MQTT
Temperature(pub=device, sub=controller):
Publish temperature(C) measurements periodically
Humidity(pub=device, sub=controller):
Publish humidity(%) measurements periodically

## Slide 5: CoAP
WaterSpurt
PUT mode=on/off : turns on or off the sprinkler

## Slide 6: Data Encoding
{
“node”:”NodeID”
“temperature”:”temperature”
}
{
“node”:”NodeID”
“humidity”:”humidityLevel”
}
All sensors return the data they have collected in JSON format.
JSON is more flexible and less verbose than XML
The application does not process a critical data